## Slide 1: AllJoyn.js Feature/Project

## Slide 2: What is AllJoyn.js?
AllJoyn + Javascript
  ECMAScript (Javascript) language interpreter and compiler for small IoT devices
  Integrate AllJoyn onboarding and config, notifications, control panel, events/actions
  Provide for OTA installation of script files
  Enable remote debugging over existing AllJoyn physical transports. (No JTAG, No USB)
Native code support
  Easily integrate native code (C/C++) with ES into compiled executable for target device
High-level programming constructs
  Portable
  Built-in regular expression engine
  Built-in Unicode support
Hardware support
  Language extensions or new functions included for interaction with hardware interfaces typically found on microcontrollers (GPIO, PWM, I2C, SPI, ADC, DAC)
Compact footprint
  128KB RAM, 500KB Flash
AllJoyn.js
AllJoyn Core +Services
ECMAScript Engine
Hardware Abstraction Layer
GPIO
SPI
PWM
ADC
I2C
I2S
DAC
UART

## Slide 3: Why is it important?
Leverage large Javascript developer community for IOT applications
  Maker community driving a lot of innovation and major shift in product development for IOT
Simplify IOT application development
  Embedded C development experience not required
  Simplified AllJoyn setup & access to service frameworks
  Simplified access to hardware (GPIO, SPI, I2C, PWM, ADC, DAC)
    Device drivers can be written in C or ES and called from ES
Portable
  User code can be moved to different devices that support AllJoyn.js
    No recompilation of ES code
      Will require native code (if used) to be re-compiled for new target
    Will require pin mapping tables to be updated
pb=IO.pin("C6", IO.PullDown); pb.trigger(IO.FallingEdge,
function(){
AJ.notification(AJ.notification.INFO, "Button Pushed!").emit(100);
});
Code for sending AJ Notification on button press
var cp = AJ.controlPanel(); var c1 = cp.containerWidget(cp.VERTICAL, cp.HORIZONTAL); var bright = c1.propertyWidget(cp.SLIDER, 50, "Brightness:"); bright.range = { min: 0, max: 100, increment: 2, units: "percent" }; var brightness = 0.5; var led = IO.pin(1, IO.Output); bright.onValueChanged = function (val) { led.pwm(1 - (bright.value / 100), 200); }
Code for exposing Control Panel slider to change LED brightness
It’s all about Time-To-Market

## Slide 4
For more information on AllSeen Alliance, visit us at: allseenalliance.org & allseenalliance.org/news/blogs